## Slide 1: Instruction Cycle

## Slide 2: Instruction Cycle
A program residing in the memory unit of the computer consists of a sequence of instructions.
. The program is executed in the computer by going through a cycle for each instruction
In the basic computer each instruction cycle consists of the following phases:
1. Fetch an instruction from memory.
2. Decode the instruction.
3. Read the effective address from memory if the instruction has an indirect address.
4. Execute the instruction.

## Slide 3: Fetch and Decode
Initially, the program counter PC is loaded with the address of the first instruction in the program.
The sequence counter SC is cleared to 0, providing a decoded timing signal To. After each clock pulse, SC is incremented by one, so that the timing signals go through a sequence T0, T1, T2, and so on. The microoperations for the fetch and decode phases can be specified by the following register transfer statements.

## Slide 4
T0: AR <- PC
T,: IR <-M[AR], PC <- PC + 1
T2: D0, • • • , D7 <- Decode IR(12-14), AR <--- IR(0-11), 1 <--- IR(lS)