## Slide 1: Instruction Format

## Slide 2: Instruction Format
The operation code field of an instruction is a group of bits that define
various processor operations, such as add, subtract, complement, and shift.
The bits that define the mode field of an instruction code specify a variety of alternatives for choosing the operands from the given address.
Here we will discuss the address field of an instruction format and consider the effect of including multiple address fields in an instruction.

## Slide 3: CPU Organization
Computers may have instructions of several different lengths containing varying number of addresses.
The number of address fields in the instruction format of a computer depends on the internal organization of its registers.
Most computers fall into one of three types of CPU organizations:
1. Single accumulator organization.
2. General register organization.
3. Stack organization.

## Slide 4: Instruction Format
The instruction format in this type of computer uses one address field. For example, the instruction that specifies an arithmetic addition is defined by an assembly language instruction as
A D D X
where X is the address of the operand. The ADD instruction in this case results in the operation AC <--AC + M [X]. AC is the accumulator register and M [X]symbolizes the memory word located at address X.
. The instruction format in this type of computer needs three register address fields. Thus the instruction for an arithmetic addition may be written in an assembly language as
A D D R 1 , R 2 , R 3
t o denote the operation R 1 <--- R2 + R 3 . The number o f address fields in the instruction can be reduced from three to two if the destination register is the same as one of the source registers. Thus the instruction
A D D R 1 , R 2 would denote the operation R 1 <--- R 1 + R2. Only register addresses for R 1 and R2 need be specified in this instruction.
Computers with multiple processor registers use the move instruction with a mnemonic MOV to symbolize a transfer instruction. Thus the instruction
M O V R 1 , R 2 denotes the transfer R 1 <--R2 (or R2 <--R 1 , depending o n the particular computer).
Thus transfer-type instructions need two address fields to specify the source and the destination.

## Slide 5
General two or three address fields in their instruction format.
A D D R 1 , X would specify the operation Rl <--R l + M [X]. It has two address fields, one for register R 1 and the other for the memory address X .
Computers with stack organization would have PUSH and POP instructions which require an address field. Thus the instruction
P U S H X will push the word at address X to the top of the stack. The stack pointer is updated automatically. Operation-type instructions do not need an address field in stack-organized computers. This is because the operation is performed on the two items that are on top of the stack
ADD in a stack computer consists o f a n operation code only with no address field. This operation has the effect of popping the two top numbers from the stack, adding the numbers, and pushing the sum into the stack.
stack pointer and instructions to push and pop from a memory stack. The processor, however, does not have the zero-address-type instructions which are characteristic of a stack-organized CPU.

## Slide 6: Three-Address Instructions
The program in assembly language that evaluates X = (A + B) • (C + D) is shown below,
A DD R 1 , A , B R 1 <--M [ A ] + M [ B ]
ADD R 2 , C , D R 2 <--M [ C ] + M [ D ]
MUL X , R 1 , R 2 M [ X ] <--R 1 • R 2

## Slide 7: Advantage and Disadvantage
The advantage o f the three-address format is that it results in short programs when evaluating arithmetic expressions. The disadvantage is that the binary-coded instructions require too many bits to specify three addresses.

## Slide 8: Two-Address Instructions
Two-address instructions are the most common in commercial computers. Here again each address field can specify either a processor register or a memory word.
The program to evaluate X = (A + B) • (C + D) is as follows.

## Slide 10
The MOV instruction moves or transfers the operands to and from memory and processor registers.
The first symbol listed in an instruction is assumed to be both a source and the destination where the result of the operation is transferred.

## Slide 11: One-Address Instructions
One-address instructions use an implied accumulator (AC) register for all data manipulation.
For multiplication and division there is a need for a second register. However, here we will neglect the second register and assume that the AC contains the result of all operations.
The program to evaluate
X = (A + B) • (C + D) is

## Slide 13
All operations are done between the AC register and a memory operand. T is the address of a temporary memory location required for storing the intermediate result.

## Slide 14: Zero-Address Instructions
A stack-organized computer does not use an address field for the instructions ADD and MUL.
The PUSH and POP instructions, however, need an address field to specify the operand that communicates with the stack.
The following program shows how X = (A + B) • (C + D) will be written for a stack organized computer.