## Slide 1: UNIT-I Introduction to Computer System Architecture

## Slide 2: Content
Von Neumann Architecture
Moores Law
Memory system
Memory Location and Address
Binary Number system
Introduction to Logic Gates
K Map
Combination Logic
Sequential Logics

## Slide 3: What is a digital computer ?
A digital computer is a machine composed of the following three basic components
  Input/Output
  Central Processing Unit (CPU)
  Memory

## Slide 4: The Von Neumann Machine, 1945
All computers more or less based on the same basic design, the Von Neumann Architecture!

## Slide 5: The Von Neumann Machine, 1945
  The Von Neumann model consists of five major components:
    input unit
    output unit
    ALU
    memory unit
    control unit.
  Sequential Execution

## Slide 6: The Von Neumann Architecture
Memory
Processor (CPU)
Input-Output
Control Unit
ALU
Store data and program
Execute program
Do arithmetic/logic operations requested by program
Communicate with
"outside world", e.g.
Screen
Keyboard
Storage devices
...
Bus

## Slide 7: Memory Subsystem
Memory, also called RA (Random Access Memory),
  Consists of many memory cells (storage units) of a fixed size. Each cell has an address associated with it: 0, 1, …
  All accesses to memory are to a specified address. A cell is the minimum unit of access (fetch/store a complete cell).
  The time it takes to fetch/store a cell is the same for all cells.
When the computer is running, both
  Program
  Data (variables)
are stored in the memory.

## Slide 8: RAM
Need to distinguish between
  the address of a memory cell and the content of a memory cell
Memory width (W):
  How many bits is each memory cell, typically one byte (=8 bits)
Address width (N):
  How many bits used to represent each address, determines the maximum memory size = address space
  If address width is N-bits, then address space is 2N (0,1,...,2N-1)
...
0
1
2
2N-1
1 bit
W
0000000000000001
N
2N

## Slide 9: Memory Size / Speed
Typical memory in a personal computer (PC):
  64MB - 256MB
Memory sizes:
  Kilobyte (KB) = 210 = 1,024 bytes ~ 1 thousand
  Megabyte(MB) = 220 = 1,048,576 bytes ~ 1 million
  Gigabyte (GB) = 230 = 1,073,741,824 bytes ~ 1 billion
Memory Access Time (read from/ write to memory)
  50-75 nanoseconds (1 nsec. = 0.000000001 sec.)
RAM is
  volatile (can only store when power is on)
  relatively expensive

## Slide 10: Operations on Memory
Fetch (address):
  Fetch a copy of the content of memory cell with the specified address.
  Non-destructive, copies value in memory cell.
Store (address, value):
  Store the specified value into the memory cell specified by address.
  Destructive, overwrites the previous value of the memory cell.
The memory system is interfaced via:
  Memory Address Register (MAR)
  Memory Data Register (MDR)
  Fetch/Store signal

## Slide 11: Structure of the Memory Subsystem
Fetch(address)
  Load address into MAR.
  Decode the address in MAR.
  Copy the content of memory cell with specified address into MDR.
Store(address, value)
  Load the address into MAR.
  Load the value into MDR.
  Decode the address in MAR
  Copy the content of MDR into memory cell with the specified address.
MAR
MDR
...
Memory
decoder
circuit
Fetch/Store
controller
F/S

## Slide 12: Input/Output Subsystem
Handles devices that allow the computer system to:
  Communicate and interact with the outside world
    Screen, keyboard, printer, ...
  Store information (mass-storage)
    Hard-drives, floppies, CD, tapes, …
Mass-Storage Device Access Methods:
  Direct Access Storage Devices (DASDs)
    Hard-drives, floppy-disks, CD-ROMs, ...
  Sequential Access Storage Devices (SASDs)
    Tapes (for example, used as backup devices)

## Slide 13: I/O Controllers
Speed of I/O devices is slow compared to RAM
  RAM ~ 50 nsec.
  Hard-Drive ~ 10msec. = (10,000,000 nsec)
Solution:
  I/O Controller, a special purpose processor:
    Has a small memory buffer, and a control logic to control I/O device (e.g. move disk arm).
    Sends an interrupt signal to CPU when done read/write.
  Data transferred between RAM and memory buffer.
  Processor free to do something else while I/O controller reads/writes data from/to device into I/O buffer.

## Slide 14: Structure of the I/O Subsystem
I/O controller
I/O Buffer
Control/Logic
I/O device
Data from/to memory
Interrupt signal (to processor)

## Slide 15: The ALU Subsystem
The ALU (Arithmetic/Logic Unit) performs
  mathematical operations (+, -, x, /, …)
  logic operations (=, <, >, and, or, not, ...)
In today's computers integrated into the CPU
Consists of:
  Circuits to do the arithmetic/logic operations.
  Registers (fast storage units) to store intermediate computational results.
  Bus that connects the two.

## Slide 16: Structure of the ALU
Registers:
  Very fast local memory cells, that store operands of operations and intermediate results.
  CCR (condition code register), a special purpose register that stores the result of <, = , > operations
ALU circuitry:
  Contains an array of circuits to do mathematical/logic operations.
Bus:
  Data path interconnecting the registers to the ALU circuitry.
ALU circuitry
GT
EQ
LT
R0
R1
R2
Rn

## Slide 17: The Control Unit
Program is stored in memory
  as machine language instructions, in binary
The task of the control unit is to execute programs by repeatedly:
  Fetch from memory the next instruction to be executed.
  Decode it, that is, determine what is to be done.
  Execute it by issuing the appropriate signals to the ALU, memory, and I/O subsystems.
  Continues until the HALT instruction

## Slide 18: Logic Gates
Types of Basic Logic Blocks
- Combinational Logic Block
Logic Blocks whose output logic value depends only on the input logic values
- Sequential Logic Block
Logic Blocks whose output logic value depends on the input values and the state (stored information) of the blocks
Gate
.
.
.
Binary
Digital
Input
Signal
Binary
Digital
Output
Signal

## Slide 19: COMBINATIONAL GATES
A
X X = (A + B)’
B
Name Symbol Function Truth Table
AND
A X = A • B
X or
B X = AB
0 0 0
0 1 0
1 0 0
1 1 1
0 0 0
0 1 1
1 0 1
1 1 1
OR
A
X X = A + B
B
I
A X X = A’
0 1
1 0
Buffer A X X = A
A X
0 0
1 1
NAND
A
X X = (AB)’
B
0 0 1
0 1 1
1 0 1
1 1 0
NOR
0 0 1
0 1 0
1 0 0
1 1 0
XOR
Exclusive OR
A X = A  B
X or
B X = A’B + AB’
0 0 0
0 1 1
1 0 1
1 1 0
A X = (A  B)’
X or
B X = A’B’+ AB
0 0 1
0 1 0
1 0 0
1 1 1
XNOR
Exclusive NOR
or Equivalence
A B X
A B X
A X
A B X
A B X
A B X
A B X

## Slide 20: BOOLEAN ALGEBRA
Boolean Algebra
* Algebra with Binary(Boolean) Variable and Logic Operations
* Boolean Algebra is useful in Analysis and Synthesis of Digital Logic Circuits
- Input and Output signals can be
represented by Boolean Variables, and
- Function of the Digital Logic Circuits can be represented by
Logic Operations, i.e., Boolean Function(s)
- From a Boolean function, a logic diagram
can be constructed using AND, OR, and I
Truth Table
* The most elementary specification of the function of a Digital Logic
Circuit is the Truth Table
- Table that describes the Output Values for all the combinations
of the Input Values, called MINTERMS
- n input variables → 2n minterms
Boolean Algebra

## Slide 21: BASIC IDENTITIES OF BOOLEAN ALGEBRA
[1] x + 0 = x
[3] x + 1 = 1
[5] x + x = x
[7] x + x’ = 1
[9] x + y = y + x
[11] x + (y + z) = (x + y) + z
[13] x(y + z) = xy +xz
[15] (x + y)’ = x’y’
[17] (x’)’ = x
[2] x • 0 = 0
[4] x • 1 = x
[6] x • x = x
[8] x • X’ = 0
[10] xy = yx
[12] x(yz) = (xy)z
[14] x + yz = (x + y)(x + z)
[16] (xy)’ = x’ + y’
[15] and [16] : De Morgan’s Theorem

## Slide 22: LOGIC CIRCUIT DESIGN
x y z F
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 0
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 1
F = x + y’z
Boolean Algebra
x
y
z
F
Truth
Table
Boolean
Function
Logic
Diagram

## Slide 23: EQUIVALENT CIRCUITS
F = ABC + ABC’ + A’C .......…… (1)
= AB(C + C’) + A’C [13] ..…. (2)
= AB • 1 + A’C [7]
= AB + A’C [4] ...…. (3)
(1)
(2)
(3)
A
B
C
F
A
B
C
F
F
A
B
C

## Slide 24: SIMPLIFICATION
Truth
Table
Boolean
Function
Unique
Many different expressions exist
Simplification from Boolean function
- Finding an equivalent expression that is least expensive to implement
- For a simple function, it is possible to obtain a simple expression for low cost implementation
- But, with complex functions, it is a very difficult task
Karnaugh Map (K-map) is a simple procedure for simplifying Boolean expressions.
Truth
Table
Boolean
function
Karnaugh
Map
Simplified
Boolean
Function

## Slide 25: KARNAUGH MAP
Karnaugh Map for an n-input digital logic circuit (n-variable sum-of-products
form of Boolean Function, or Truth Table) is
- Rectangle divided into 2n cells
- Each cell is associated with a Minterm
- An output(function) value for each input value associated with a mintern is written in the cell representing the minterm
→ 1-cell, 0-cell
Each Minterm is identified by a decimal number whose binary representation is identical to the binary interpretation of the input values of the minterm.
Karnaugh Map
x F
0 1
1 0
x
0
1
0
1
x
0
1
0
1
value
of F
Identification
of the cell
x y F
0 0 0
0 1 1
1 0 1
1 1 1
y
x
0 1
0
1
0 1
2 3
y
x
0 1
0
1
0 1
1 0
F(x) =
F(x,y) =  (1,2)
1-cell
 (1)

## Slide 26: KARNAUGH MAP
0 0 0 0
0 0 1 1
0 1 0 1
0 1 1 0
1 0 0 1
1 0 1 0
1 1 0 0
1 1 1 0
0 1 0 1
1 0 0 0
0 0 0 0 0
0 0 0 1 1
0 0 1 0 0
0 0 1 1 1
0 1 0 0 0
0 1 0 1 0
0 1 1 0 1
0 1 1 1 0
1 0 0 0 1
1 0 0 1 1
1 0 1 0 0
1 0 1 1 1
1 1 0 0 0
1 1 0 1 0
1 1 1 0 1
1 1 1 1 0
x
yz
00 01 11 10
0
0 1 3 2
4 5 7 6
x
yz
00 01 11 10
0
1
F(x,y,z) =  (1,2,4)
1
x
y
z
uv
wx
00 01 11 10
00
01
11
10
0 1 3 2
4 5 7 6
12 13 15 14
8 9 11 10
uv
wx
00 01 11 10
00
01
11 0 0 0 1
10 1 1 1 0
0 1 1 0
0 0 0 1
F(u,v,w,x) =  (1,3,6,8,9,11,14)
u
v
w
x
Map Simplification
x y z F
u v w x F

## Slide 27: MAP SIMPLIFICATION - 2 ADJACENT CELLS -
Adjacent cells
- binary identifications are different in one bit
→ minterms associated with the adjacent
cells have one variable complemented each other
Cells (1,0) and (1,1) are adjacent
Minterms for (1,0) and (1,1) are
x • y’ --> x=1, y=0
x • y --> x=1, y=1
F = xy’+ xy can be reduced to F = x
From the map
Rule: xy’ +xy = x(y+y’) = x
x
y
0 1
0
1
1 1
0 0
 (2,3)
F(x,y) =
2 adjacent cells xy’ and xy
→ merge them to a larger cell x
= xy’+ xy
= x

## Slide 28: MAP SIMPLIFICATION - MORE THAN 2 CELLS -
u’v’w’x’ + u’v’w’x + u’v’wx + u’v’wx’
= u’v’w’(x’+x) + u’v’w(x+x’)
= u’v’w’ + u’v’w
= u’v’(w’+w)
= u’v’
uv
wx
1 1 1 1
1 1
1 1
uv
wx
1 1 1 1
1 1
1 1
u
v
w
x
u
v
w
x
u’v’
uw
u’x’
v’x
1 1
1 1
vw’
u’v’w’x’+u’v’w’x+u’vw’x’+u’vw’x+uvw’x’+uvw’x+uv’w’x’+uv’w’x
= u’v’w’(x’+x) + u’vw’(x’+x) + uvw’(x’+x) + uv’w’(x’+x)
= u’(v’+v)w’ + u(v’+v)w’
= (u’+u)w’ = w’
u
v
w
x
uv
wx
1 1
1 1
1 1
1 1
u
v
uv
1 1
1 1
1 1
1 1
1 1 1 1
x
w’
u
V’
w

## Slide 29: MAP SIMPLIFICATION
(0,1), (0,2), (0,4), (0,8)
Adjacent Cells of 1
Adjacent Cells of 0
(1,0), (1,3), (1,5), (1,9)
...
...
Adjacent Cells of 15
(15,7), (15,11), (15,13), (15,14)
uv
wx
00 01 11 10
00
01 0 0 0 0
11 0 1 1 0
10 0 1 0 0
1 1 0 1
F(u,v,w,x) =  (0,1,2,9,13,15)
u
v
w
x
Merge (0,1) and (0,2)
--> u’v’w’ + u’v’x’
Merge (1,9)
--> v’w’x
Merge (9,13)
--> uw’x
Merge (13,15)
--> uvx
F = u’v’w’ + u’v’x’ + v’w’x + uw’x + uvx
But (9,13) is covered by (1,9) and (13,15)
F = u’v’w’ + u’v’x’ + v’w’x + uvx
0
0
0
0
1
1
0
1
0
1
1
0
0
1
0
0

## Slide 30: IMPLEMENTATION OF K-MAPS - Sum-of-Products Form -
Logic function represented by a Karnaugh map
can be implemented in the form of I-AND-OR
A cell or a collection of the adjacent 1-cells can
be realized by an AND gate, with some inversion of the input variables.
x
y
z
x’
y’
z’
x’
y
z’
x
y
z’
1
1
1
F(x,y,z) =  (0,2,6)
1 1
1
x’
z’
y
z’

x’
y
x
y
z’
x’
y’
z’
F
x
z
y
z
F
I AND OR
z’


## Slide 31: IMPLEMENTATION OF K-MAPS - Product-of-Sums Form -
Logic function represented by a Karnaugh map
can be implemented in the form of I-OR-AND
If we implement a Karnaugh map using 0-cells,
the complement of F, i.e., F’, can be obtained.
Thus, by complementing F’ using DeMorgan’s
theorem F can be obtained
F(x,y,z) = (0,2,6)
x
y
z
x
y’
z
F’ = xy’ + z
F = (xy’)z’
= (x’ + y)z’
x
y
z
F
I OR AND
0
0
1
1
0
0
0
1

## Slide 32: IMPLEMENTATION OF K-MAPS - Don’t-Care Conditions -
In some logic circuits, the output responses
for some input conditions are don’t care
whether they are 1 or 0.
In K-maps, don’t-care conditions are represented
by d’s in the corresponding cells.
Don’t-care conditions are useful in minimizing
the logic functions using K-map.
- Can be considered either 1 or 0
- Thus increases the chances of merging cells into the larger cells
--> Reduce the number of variables in the product terms
x
y
z
1 d d 1
d 1
x’
yz’
x
y
z
F

## Slide 33: Combination Logic
Half Adder
0 0 0 0 0
0 0 1 0 1
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 1
cn = xy + xcn-1+ ycn-1
= xy + (x  y)cn-1
s = x’y’cn-1+x’yc’n-1+xy’c’n-1+xycn-1
= x  y  cn-1 = (x  y)  cn-1
x
y
cn-1
x
y
cn-1
cn
s
x
y
x
y
c = xy s = xy’ + x’y
= x  y
x
y
c
s
x
y
cn-1
S
cn
Full Adder
0 0 0 0
0 1 0 1
1 0 0 1
1 1 1 0
x y c s
0
1
0
0
0
0
1
1
x y cn-1 cn s
0
0
1
0
0
1
1
1
0
1
0
1
1
0
1
0

## Slide 34: MULTIPLEXER
4-to-1 Multiplexer
I0
I1
I2
I3
S0
S1
Y
0 0 I0
0 1 I1
1 0 I2
1 1 I3
Select Output
S1 S0 Y

## Slide 35: ENCODER/DECODER
Octal-to-Binary Encoder
D1
D2
D3
D5
D6
D7
D4
A0
A1
A2
A0
A1
E
D0
D1
D2
D3
0 0 0 0 1 1 1
0 0 1 1 0 1 1
0 1 0 1 1 0 1
0 1 1 1 1 1 0
1 d d 1 1 1 1
E A1 A0 D0 D1 D2 D3
2-to-4 Decoder

## Slide 36: Sequential Logic & The Flip-Flop
Combinational
Logic Gates
.
.
Inputs
Outputs
Memory Elements
(Flip-Flops)
.
.
Clock
Notes: Definition of sequential logic. Sequential logic can have one or more, inputs and one or more outputs. However, the outputs are a function of both the present value of the inputs and also the previous output values. Thus, sequential logic requires memory to store these previous outputs values.

## Slide 37: Flip-flop Characteristic Tables
JK Flip-flop
SR Flip-flop
D Flip-flop
T Flip-flop

## Slide 38: CLOCKED FLIP FLOPS
In a large digital system with many flip flops, operations of individual flip flops
are required to be synchronized to a clock pulse. Otherwise,
the operations of the system may be unpredictable.
R
S
Q
Q’
c
(clock)
Flip Flops
S Q
c
R Q’
S Q
c
R Q’
operates when operates when
clock is high clock is low
Clock pulse allows the flip flop to change state only
when there is a clock pulse appearing at the c terminal.
We call above flip flop a Clocked RS Latch, and symbolically as

## Slide 39: RS-LATCH WITH PRESET AND CLEAR INPUTS
Flip Flops
R
S
Q
Q’
c
(clock)
P(preset)
clr(clear)
S Q
c
R Q’
S Q
c
R Q’
P
clr
P
clr
S Q
c
R Q’
P
clr
S Q
c
R Q’
P
clr

## Slide 40: D-LATCH
D-Latch
Forbidden input values are forced not to occur
by using an inverter between the inputs
Flip Flops
Q
Q’
D(data)
E
(enable)
D Q
E Q’
E Q’
D Q
D Q(t+1)
0 0
1 1

## Slide 41: EDGE-TRIGGERED FLIP FLOPS
Characteristics
- State transition occurs at the rising edge or
falling edge of the clock pulse
Latches
Edge-triggered Flip Flops (positive)
respond to the input only during these periods
respond to the input only at this time
Flip Flops

## Slide 42: POSITIVE EDGE-TRIGGERED
T-Flip Flop: JK-Flip Flop whose J and K inputs are tied together to make
T input. Toggles whenever there is a pulse on T input.
Flip Flops
D-Flip Flop
JK-Flip Flop
S1 Q1
C1
R1 Q1'
S2 Q2
C2
R2 Q2'
D
C
Q
Q'
D
C
Q
Q'
SR1 SR2
SR1 active
SR2 active
D-FF
S1 Q1
C1
R1 Q1'
S2 Q2
C2
R2 Q2'
SR1 SR2
J
K
C
Q
Q'
J Q
C
K Q'
SR1 active
SR2 inactive
SR2 inactive
SR1 inactive

## Slide 43: CLOCK PERIOD
Clock period determines how fast the digital circuit operates.
How can we determine the clock period ?
Usually, digital circuits are sequential circuits which has some flip flops
Combinational
Logic
Circuit
FF
FF
Combinational logic Delay
FF Setup Time
FF Hold Time
FF Delay
td
ts,th
clock period T = td + ts + th
Flip Flops
.
.
.
...
FF
C
Combinational
Logic
Circuit
FF
FF
.
.
.